## Slide 1: Orientation for TECHNITIAN engineers
Road inventory and condition survey
By
Ing. Franklin a. Agbanator
(ktc)
4TH – 6TH October 2018

## Slide 2: outline
Introduction
What is road inventory and condition survey
Why do we undertake this activities
  Benefits
  The lacks
WHAT DATA TO COLLECT
How it is done
conclusion

## Slide 3: introduction
Every infrastructure require maintenance
Every meaningful maintenance must be based on the real time condition of the infrastructure
Different types of data are required for managing transportation infrastructure. Data collection technologies and data needs vary depending on which infrastructure element is evaluated.
In the road infrastructure, regular inspection and accurate data collection is required for reliable and informed maintenance decisions

## Slide 4: What is road inventory and condition survey
The process of getting the data that is needed to make informed decisions about the road network. Well documented validation, verification and quality systems ensure easy collection and reliable end results.
There are many technologies for the collection of data, but the data that is beneficial to the transportation agency in question as well as the appropriate equipment to be used to collect these data need to be decided.
These surveys are done to determine the condition of the pavement sub layers and the location of dangerous voids.

## Slide 5: Why do we undertake this activities
The survey is conducted annually for budget planning and quantity assessment of maintenance works based on the conditions of target roads
The data collected should support the following objectives:
  Provide the data required to support the approach to asset management
  Describe the asset and its performance
  Provide the basis for informed decision making
  Facilitate communications with stakeholders
  Inform the assessment and management of risk
  Support the management of statutory requirements
  Support continuous improvement

## Slide 6: What data to collect?
The data needed by any transportation agency are those that influence
  The cost to replace or maintain road assets,
  Maintenance or rehabilitation treatment options,
  Influences on management decisions, and
  Service life.
In principle, asset management data falls into two main types and can be grouped as follows:
  Inventory data: Data that are mostly static in nature and describe the physical element of the road system and
  road assets Condition data: Data that describe the condition of the assets; these data markedly change over time

## Slide 7: What data to collect?
Other data used for transportation asset management can be grouped as follows:
  Traffic data
  Financial data
  Asset management activities data
  Resource allocation data

## Slide 8: WHAT DATA TO COLLECT
TYPES OF ROADS |  |  |  |  |  |  | 
ROAD CHARACTERISTIC DATA | LIMITED ACCESS |  | ARTERIALS |  | COLLECTORS |  | LOCALS
CROSS SECTION ELEMENTS |  |  |  |  |  |  | 
NUMBER OF LANES |  |  |  |  |  |  | 
LANE WIDTH |  |  |  |  |  |  | 
LANE TYPE |  |  |  |  |  |  | 
SHOULDER WIDTH |  |  |  |  |  |  | 
SHOULDER TYPE |  |  |  |  |  |  | 
EDGE TREATMENTS(EDGE SAFETY) |  |  |  |  |  |  | 
MEDIAN WIDTH |  |  |  |  |  |  | 
MEDIAN TYPE |  |  |  |  |  |  | 
ROW WIDTH |  |  |  |  |  |  | 
CROSS SLOPE (NORMAL CROWN) |  |  |  |  |  |  | 
BARRIERS (TYPES , LENGTH) |  |  |  |  |  |  | 
ETC ETC ETC |  |  |  |  |  |  | 

## Slide 9: WHAT DATA TO COLLECT
TYPES OF ROADS |  |  |  |  |  |  | 
ROAD CHARACTERISTIC DATA | LIMITED ACCESS |  | ARTERIALS |  | COLLECTORS |  | LOCALS
ROADWAY STRUCTURE ELEMENTS |  |  |  |  |  |  | 
BRIDGES |  |  |  |  |  |  | 
RAILROAD CROSSING |  |  |  |  |  |  | 
MULTI – USED PATH / BIKE PATH |  |  |  |  |  |  | 
PEDESTRIAN FACILITIES |  |  |  |  |  |  | 
TUNNELS |  |  |  |  |  |  | 
GEOMETRIC ELEMENTS |  |  |  |  |  |  | 
GRADE |  |  |  |  |  |  | 
VERTICAL CURVATURE |  |  |  |  |  |  | 
HORIZONTAL CURVATURE |  |  |  |  |  |  | 
SUPERELEVATION |  |  |  |  |  |  | 
SIGHT DISTANCE |  |  |  |  |  |  | 
SPEED LIMIT |  |  |  |  |  |  | 

## Slide 10: WHAT DATA TPO COLLECT
SIGN INVENTORY |  |  |  |  |  |  | 
TRUCK WEIGHT RESTRICTION |  |  |  |  |  |  | 
INTERSECTION ELEMENTS |  |  |  |  |  |  | 
NUMBER OF LANES / APPROACH |  |  |  |  |  |  | 
SIGNAL TIMINGS |  |  |  |  |  |  | 
TRFFIC CONTROL |  |  |  |  |  |  | 
PAVEMENT ELEMENTS |  |  |  |  |  |  | 
PAVEMENT MATERIALS |  |  |  |  |  |  | 
PAVEMENT DISTRESS DATA |  |  |  |  |  |  | 
SKID RESISTANCE |  |  |  |  |  |  | 
RIDE QUALITY |  |  |  |  |  |  | 
PAVEMENT MARKINGS |  |  |  |  |  |  | 

## Slide 11: HOW IT IS DONE
THERE ARE DIFFERENT TECHNOLOGIES AVAILABLE TODAY
ARRB offers quality data collection,
field inventory, photo/video log, integrated Global Positioning System (GPS)/Geographic Information Systems (GIS) mapping systems, aerial photography, satellite imagery, airborne Light Detection and Ranging (LiDAR), terrestrial laser scanners, and mobile LiDAR

## Slide 12: CONCLUSION
WITHOUT AN ACCURATE AND RELIABLE DATA YOUR PLAN FOR ROAD MAINTENANCE WILL SUFFER
IT IS TIME WE BEGUN TO TAKE ROAD INFRASTRUCTURE MAINTENANCE SERIOUSLY TO PRESERVE OUR AGING ASSETS

## Slide 13: THANKS FOR YOUR ATTENTION